## Slide 1: PROCESSING OPERATIONS IN PRACTICE
CHAPTER 30

## Slide 2: ASRT Objective
Associate impact of image processing parameters to the image appearance.
Formulate a procedure or process to minimize histogram analysis and rescaling errors. (SEE PAGE 586)

## Slide 3: Speed
Elsevier items and derived items © 2008 by Mosby, Inc., an affiliate of Elsevier Inc.
<number>
In CR, most cassettes have the same speed; however, there are special extremity or chest cassettes that produce greater resolution.
These are typically 200 relative speed.
Notes: <number>
WHY DOES THIS CHAPTER TALK ABOUT THE SPEED OF THE DETECTOR?
THE SPEED IS DETERMINED BY HOW EFFICIENTLY THE DETECTOR/DR CASSETTE CONVERTS X-RAY PHOTONS INTO ELECTRONIC DATA.
THE FASTER THE SPEED, THE LESS PHOTONS ARE NEEDED TO CONVERT, BUT THE LESS RESOLUTION YOU WILL HAVE.

## Slide 4: OTHER THINGS THAT CAN AFFECT THE IMAGE SENT TO PACS: Magnification
Elsevier items and derived items © 2008 by Mosby, Inc., an affiliate of Elsevier Inc.
<number>
  Other technique is “zoom.”
  Zoom allows magnification of the entire image.
  Image can be enlarged enough that only parts of it are visible on the screen.
  Those parts can be seen through mouse navigation.
Notes: <number>
GENERALLY NOT PERMANENT

## Slide 5: OTHER THINGS THAT CAN AFFECT THE IMAGE SENT TO PACS: Smoothing
Elsevier items and derived items © 2008 by Mosby, Inc., an affiliate of Elsevier Inc.
<number>
Notes: <number>
GENERALLY SIGNALS FROM EACH PIXEL ARE AVERAGED TOGETHER. THE MORE PIXELS INVOLVED IN THE CALCULATION, THE SMOOTHER THE PICTURE APPEARS. WITH SMOOTHING, MORE PIXELS ARE AVERAGED TOGETHER.
Result is a reduction of noise and contrast.
Low-pass filtering is useful for viewing small structures such as fine bone tissues.

## Slide 6: OTHER THINGS THAT CAN AFFECT THE IMAGE SENT TO PACS: Edge Enhancement
Elsevier items and derived items © 2008 by Mosby, Inc., an affiliate of Elsevier Inc.
<number>
Notes: <number>
USED TO BRING OUT THE OUTLINES
GENERALLY PRODUCES A SHORTER SCALE OF CONTRAST AND MAKES EDGES APPEAR SHARPER
GENERALLY SIGNALS FROM EACH PIXEL ARE AVERAGED TOGETHER. THE MORE PIXELS INVOLVED IN THE CALCULATION, THE SMOOTHER THE PICTURE APPEARS. WITH EDGE ENHANCEMENT, FEWER PIXELS ARE AVERAGED TOGETHER.
ALSO KNOWN AS HIGH PASS FILTERING
CAN RESULT IN LOSS OF DETAIL OR INFORMATION – SHOULD ONLY BE USED WHILE VIEWING ( POST PACS)

## Slide 7: Example of Edge Enhancement, B

## Slide 8: OTHER THINGS THAT CAN AFFECT THE IMAGE SENT TO PACS: Black Masking

## Slide 9: Collimation vs. Shuttering
Elsevier items and derived items © 2008 by Mosby, Inc., an affiliate of Elsevier Inc.
<number>
This results in increased contrast because of the reduction of scatter as fog and reduces the amount of grid cleanup necessary for increased resolution.
Through post exposure image manipulation known as shuttering, a black background can be added around the original collimation edges, virtually eliminating the distracting white or clear areas.
Notes: <number>
Insufficient collimation results in unattenuated radiation striking the imaging plate.
The resulting histogram is changed so that it is outside the normal exposure indicator range for the part selected.
Using the smallest imaging plate possible and proper collimation, especially on small or thin patients, eliminates this error.

## Slide 10: OTHER THINGS THAT CAN AFFECT THE IMAGE SENT TO PACS: Image Reversal

## Slide 11: OTHER THINGS THAT CAN AFFECT THE IMAGE SENT TO PACS: Image Annotation
Elsevier items and derived items © 2008 by Mosby, Inc., an affiliate of Elsevier Inc.
<number>
Annotations overlay the image as bitmap images.
Annotations may not transfer to picture archival and communication system (PACS).
Input of annotation for identification of the patient’s left or right side should never be used as a substitute for technologist’s anatomy markers.
Notes: <number>
Information other than standard identification must be added to the image.
In screen/film radiography, additional information is marked by the following:
  Time and date stickers
  Grease pencils
  Permanent markers

## Slide 12: OTHER THINGS THAT CAN AFFECT THE IMAGE: Image Stitching
Elsevier items and derived items © 2008 by Mosby, Inc., an affiliate of Elsevier Inc.
<number>
Images are processed in computer programs that nearly seamlessly join the anatomy.
Computer displays one single image.
Process eliminates the need for large (36-inch) cassettes previously used in film/screen radiography.
Notes: <number>
Stitching is used for anatomy or areas of interest too large to fit on one cassette.
Multiple images can be “stitched” together.
Sometimes, special cassette holders are used and positioned vertically, corresponding to foot to hip or entire spine radiography.

## Slide 13
CR Scoliosis Series
Image Stitching feature shows seam lines between 3 images

## Slide 14: OTHER THINGS THAT CAN AFFECT THE IMAGE: Alternative Algorithms
One way to adjust the contrast and brightness characteristics of an image is to re-process it under a different pre-set anatomical algorithm
Right: A lateral lumbar spine re-processed as a thoracic spine shows improved visibility of those vertebrae within the lung field

## Slide 15: Exposure Indicator Errors
Anything which can lead to histogram analysis errors can cause the exposure indicator to be corrupted
  Extraneous exposure information, including scatter
  Exposure field recognition error
  Unexpected material in field
  Collimation margins not detected
  Extreme underexposure or overexposure
  Delay in processing

## Slide 16
Copyright © 2006 by Thomson Delmar Learning. ALL RIGHTS RESERVED.
<number>
Notes: <number>
POOR CR CLEANING

## Slide 17
Copyright © 2006 by Thomson Delmar Learning. ALL RIGHTS RESERVED.
<number>

## Slide 18
Copyright © 2006 by Thomson Delmar Learning. ALL RIGHTS RESERVED.
<number>
Notes: <number>
LINE DROP

## Slide 19
Copyright © 2006 by Thomson Delmar Learning. ALL RIGHTS RESERVED.
<number>
Notes: <number>
ERROR IN LUT

## Slide 20
Copyright © 2006 by Thomson Delmar Learning. ALL RIGHTS RESERVED.
<number>
Notes: <number>
CR DROP OUT

## Slide 21: Notes:
The reject button on most systems results in permanent loss of the image, making “repeat” analysis hard to perform. When prompted to enter the reason for a reject, it is important to enter an honest answer rather than “other.” Departments must find ways to make reject analysis possible, for several professional and ethical reasons.
PAY ATTENTION TO PAGE 586
Notes: <number>

## Slide 22
A computed radiography image is taken at 66 kVp and 11 mAs with a 12:1 Grid at 60 inches. The computer tries to fix the image, but the exposure index values indicate underexposure. A new image needs to be taken, but the patient has been moved and now you as the technologist can only get a 40" SID. What should the new technique be?
Notes: <number>